## Slide 1: CS683: Advanced Computer Architecture-2024
L1-Performance, Performance, and Performance
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Join Piazza if you are part of CS683

## Slide 4: Programmer’s view

## Slide 5
Let’s start with programming for Performance
(know your architecture)

## Slide 6: Performance
100,000x speedup since the first processor 
[1971:
92500 instructions per second, 640B RAM
2024:
10s of billion instructions per second, TB of RAM]
Automobile industry: really slow  Imagine tata motors providing 2X speedup every 18 months 
Game of trade-offs btw. What is the price per performance?

## Slide 7
void CS683(int *arr, int size) {
for (int i = 0; i < size-1; ++i)
arr[i] = arr[i+1];
}

## Slide 8: Performance
CPU
CPU time: Time spent running a program
CPU
Execution time: CPU time + IO waiting
CPU time: User time + System (OS) time

## Slide 9: Example
#define N 32
#define T 1024 * 1024 double A[N][N];
for (it = 0; it | < | T; it++)
for (j = 0; j | < | N; j++)
for (i = 0; | i | < N; i++)
A[i][j] += 1;
#define | N | 32 |  | 
#define | T | 1024 | * | 1024
#define | N | 128 |  | 
#define | T | 1024 | * | 1024
#define | N | 256 |  | 
#define | T | 1024 | * | 1024
#define | N | 4096 |  | 
#define | T | 1024 | * | 1024
235 ms
240 ms
420 ms
750 ms

## Slide 10: Which one is better? Why?
for (int i = 0; i < n; i++) { z[i] = x[i] – y[i];
z[i] = z[i] * z[i];
}
for (int i = 0; i < n; i++) { z[i] = x[i] – y[i];
}
for (int i = 0; i < n; i++) { z[i] = z[i] * z[i];
}
Which version is more efficient if we have large arrays?

## Slide 11: Spell it out
Instructions
Cycles
Program
Instruction
Time
Cycle
(code size)
=
X
X
(CPI)
(cycle time)

## Slide 12: Cycles per Instruction
Instructions: I mean the DYANMIC (ADD, MUL, JUMP, LOAD/STORE) ones
void CS683(int *arr, int size) {
for (int i = 0; i < size-1; ++i)
arr[i] = arr[i+1];
}
CPU
All instructions are not the SAME
So, cycles per instruction is not a constant

## Slide 13: From Theory to Practice: Performance-101

## Slide 14: Language: No Big Deal!! AI/ML && Python

## Slide 15: OK. So??

## Slide 16: Seriously??

## Slide 17: That’s It!! You can’t do better 

## Slide 18: What the hell? This is insane !!

## Slide 19
62,806X

## Slide 20: Welcome to CS683, again !!

## Slide 21: Let’s Jump into Memory Hierarchy, why?

## Slide 22: From where does these zeros come from?
L3
L1
L2
2 Cycles
12 Cycles
30 Cycles
200 Cycles
DRAM Contr.
Core
CPU
Memory stores CODE and DATA
Processor accesses through LOADs (reads) and STOREs(writes)
Memory Wall

## Slide 23: The game of latency and bandwidth starts

## Slide 24: Hang on!! I got the Mantra!!
Reduction in DRAM accesses ~
Reduction in CPI (cycles per instruction)
WRONG!
First Law of Performance:
  Make the common case fast
Second Law of Performance:
  Make the fast case common
  Amdahl’s law
What if your program is not memory intensive

## Slide 25: Do not ignore the uncommon too
Give me an example for a credit point

## Slide 26: Let’s Pause and understand: The game of “common” and “uncommon”

## Slide 27: Do not
Over-engineer
Over-think
Over …………………..

## Slide 28: 10,000 Feet View on Caches
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
$$: Cache
Speculation technique
Speculation works because of locality

## Slide 29: Caches
Hardware hash tables 
Catch the cache

## Slide 30: Summary
IPC/CPI
Latency/Bandwidth
Common case