## Slide 1: CS683: Advanced Computer Architecture-2024
L6-Cache Management Techniques and Hardware Prefetching!!
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Reducing Miss rate (MPKI)

## Slide 4: Cache Content Management
Cache Promotion Policy: On a future hit (block i), promote to MRU
LRU causes thrashing when working set > cache size
a
b
c
d
e
f
g
h
Cache Eviction Policy: On a miss (block i), which block to evict (replace) ?
MRU LRU
SET A
i
a
b
c
d
e
f
g
Cache Insertion Policy: New block i inserted into MRU.
MRU LRU
SET A

## Slide 5: Common Cache Access Patterns
Recency friendly (a1, a2,….ak, ak-1, ….a2, a1)N
Thrashing (a1, a2,….ak)N
[k > cache size]
Streaming (a1, a2,….a∞)N
Combination of above three

## Slide 6: LRU limitations
LRU exploits temporal locality
Streaming data (a1, a2, a3,….a∞): No temporal locality,
No temporal reuse
Thrashing data (a1, a2, a3,….an) [n>c] Temporal locality exists. However, LRU fails to capture.

## Slide 7: BTW, LRU is not implemented @commercial machines

## Slide 8: Bimodal Policy [ISCA ‘07]
if ( rand() <  ) 
Insert at MRU position; else
Insert at LRU position;
For small : BIP retains thrashing protection of LRU insertion policy.
Infrequently insert lines in MRU position

## Slide 9: Dynamic Insertion Policy (DIP): Celebrated technique in the community
SDM (LRU-sets)
Follower Sets
SDM (BIP-sets)
n-bit PSEL
+
miss
–
miss
MSB = 0?
YES
Use LRU
No Use BIP
SDM – Set Dueling monitors PSEL – n-bit saturating counters for deciding a policy

## Slide 10: RRIP [ISCA ‘10]
RRP Tail
3
2
1
‘intermediate’ ‘far’ ‘distant’
0
‘near-
Re-reference Prediction Value RRPV (n=2):
Qualitative Prediction:
RRP Head
h g f e d c b a
immediate’
Intuition: New cache block will not be re-referenced soon.
Replaces block with distant RRPV.
Insert with RRPV=2, Evict with RRPV=3 promote blocks with RRPV=0.
Static RRIP (Single core) and Thread-Aware Dynamic RRIP (SRRIP+BRRIP, multi-core, based on SDMs).

## Slide 11: 2-bit state machine
0
Imme- diate
1
Inter- mediate
3
distant
re-reference
No Victim
re-reference
eviction
re-reference
No 2
Victim far
No Victim
(SRRIP)
Scan-Resistant
insertion
( BRRIP )
Thrash-Resistant
insertion

## Slide 12: Reducing Miss rate, Nah, Miss Latency
Hardware Prefetching

## Slide 13: Hardware Prefetching
What?
Latency-hiding technique - Fetches data before the core demands.
Why?
Off-chip DRAM latency has grown up to 400 to 800 cycles.
How?
By observing/predicting the demand access (LOAD/STORE) patterns.

## Slide 14: An example
L2
Prefetcher
X+3
Core
❶
❷
❸
❹
❺
X+3
HIT
X+2 X+1 X

## Slide 15: Prefetch Degree
Prefetch Degree: Number of prefetch requests to issue at a given time.
L2
L3/DRAM
Prefetcher
X
Demand Access
X+1 |  |  | 
X+1 | X+2 |  | 
X+1 | X+2 | X+3 | X+4

## Slide 16: Prefetch Distance
Prefetch Distance: How far ahead of the demand access stream are the prefetch requests issued?
 |  | X |  |  | Y | 
demand
access
Prefetch-distance Y = X + 4
Y = X + 8 Y = X + 16
prefetch

## Slide 17: The Simplest one
Next Line: Miss to cache block X , prefetch X+1. Degree=1, Distance=1
Works well for L1 Icache and L1 Dcache.
Next N Line: Miss to cache block X , prefetch X+1, X+2, ….. X+N, Degree=N, Distance= min. 1 and max. N

## Slide 18: See you on August 23rd