## Slide 1: CS773-2025-Spring: Computer Architecture for Performance and Security
Lecture 11: Mitigation Techniques
(Slides adapted from Nishkarsh and Chris)

## Slide 2: Phones on silence, please Thank You

## Slide 3: Spectre Mitigations

## Slide 4: Classification of mitigation techniques
if (x < array1_size) // Mispredict
secret = array1[x]; // Access
y = array2[secret * 64]; // Transmit
array2[0]
array2[64]
array2[128] . . . // Inference
Mitigations
Invisible speculation
Delay based

## Slide 5: GhostMinion Cache [State-of-the-art, invisible speculation based ]
L1D
L2
LLC
DRAM
CPU
GM
L1D
L2
LLC
DRAM
CPU
Normal Cache hierarchy
GhostMinion
commit
Evict
Evict

## Slide 6: Invisible Speculation and then redo accesses
CPU
L1D
L2C
LLC
DRAM
SB
    Issue speculative LOADs invisibly
Speculative LOAD
Fill to SB
    No cache state change is observed
SB = Speculative Buffer or a cache
Redo step makes all speculative loads visible into the rest of the hierarchy

## Slide 7: Rigid Definition of Safety in GhostMinion
When an instruction commits then only it is secure/safe and then the address and data corresponding to that instruction are propagated into the cache hierarchy.
On a context switch, the GM cache is squashed.

## Slide 8: Block the covert channels! [Spec Taint Tracking, MICRO ’1, delay based approach]
if (x < array1_size) // Mispredict
secret = array1[x]; // Access
y = array2[secret*64]; // Transmit
Secret dep. install
CACHE
array2[0]
array2[64]
array2[128]
array[192]
Block the covert channel

## Slide 9: Speculative Execution in Action
// Spectre Variant 1
if (addr < N) { // speculation
// access instruction spec_val = load [addr];
// covert channel
load [spec_val];
}
Speculation starts

## Slide 10: Speculative Execution in Action
// Spectre Variant 1
if (addr < N) { // speculation
// access instruction spec_val = load [addr];
// covert channel
load [spec_val];
}
Speculation starts
Speculative access instruction**
accesses secret

## Slide 11: Speculative Execution in Action
// Spectre Variant 1
if (addr < N) { // speculation
// access instruction spec_val = load [addr];
// covert channel
load [spec_val];
}
Speculation starts
Creates a covert channel
to leak secret
Speculative access instruction**
accesses secret

## Slide 12: Speculative Execution in Action
// Spectre Variant 1
if (addr < N) { // speculation
// access instruction spec_val = load [addr];
// covert channel
load [spec_val];
}
Speculation starts
Creates a covert channel
to leak secret
Speculation ends -
misspeculation!
Speculative access instruction**
accesses secret

## Slide 13: What we want in terms of security?
if (addr < N) {
// access instruction spec_val = load [addr];
// simple arithmetic spec_val = spec_val + 4;
// cache/mem covert channel
load [spec_val];
}
……
Creates a covert channel? | Input operand is a secret? | Requires protection?

## Slide 14: STT in action
if (addr < N) {
// access instruction spec_val = load [addr];
// simple arithmetic spec_val = spec_val + 4;
// cache/mem covert channel
load [spec_val];
}
……
prediction
Speculation
starts
Creates a covert channel? | Input operand is a secret? | Requires protection?

## Slide 15: STT in action
if (addr < N) {
// access instruction spec_val = load [addr];
// simple arithmetic spec_val = spec_val + 4;
// cache/mem covert channel
load [spec_val];
}
……
Speculation
starts
Creates a covert channel? | Input operand is a secret? | Requires protection?
Yes | No | No

## Slide 16: STT in action
if (addr < N) {
// access instruction spec_val = load [addr];
// simple arithmetic spec_val = spec_val + 4;
// cache/mem covert channel
load [spec_val];
}
……
Speculation
starts
Creates a covert channel? | Input operand is a secret? | Requires protection?
Yes | No | No
No | Yes | No
Yes | Yes | Yes
“Sufficient for security: prevent secrets from reaching covert channels” Delay transmitting the memory accesses

## Slide 17: How to find safe as per STT?
Track branch resolutions, if resolved, even if it is transient, it will be guaranteed that it will commit. Then you can communicate the memory request to the memory hierarchy.