## Slide 1: CS773-2025-Spring: Computer Architecture for Performance and Security
Lecture 14: DRAM attacks

## Slide 2: DRAM Organization
Channel
Rank
Chip
Bank
Row
Column
Rank 0 with 8 chips
Rank 1 with 8 chips
DIMM

## Slide 3: Rank
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 4: Ranks, Banks, Rows, Columns
Rank 0
Rank 1
DIMM
Bank 0
Bank 1
Bank 2
Bank 3
Multiple Chips

## Slide 5: Ranks, Banks, Rows, Columns
Rank 0
64 bits
16
16
16
16
Bank
Row
Column
Chip
Bank 0
Bank 1
Bank 2
Bank 3
X16 device (DRAM width, # output pins)
16-bit interface: 16 bits from each chip in one go

## Slide 6: Row Decoder and Row buffer
Column mux
Row Decoder
Row Buffer
Each bank has a row buffer
Stores the last used row
2KB

## Slide 7: DRAM Address Mapping (One Channel)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
2GB DRAM, 8 Banks, 16K rows, 2K Columns per bank
Row Interleaving: Consecutive rows in consecutive banks
Cache Interleaving: Consecutive cache blocks in consecutive banks

## Slide 8: Row Buffer hit/miss/conflict
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:
ACTIVATE, PRECHARGE, and Column read are the three commands of interest

## Slide 9: Row (Page) Policies
Open Page (do not get confused with an OS page)
After an access: Keep the page in the row-buffer
Consecutive accesses to the same page : Row-buffer Hit (no ACTs)
On an access to different page: Close the row and open the new one
Closed page:
After an access: Close the page if there are no accesses to the same row in the request queue.
Consecutive accesses to different page : Low latency
On an access to different page: No need to close the row (no PREs)

## Slide 10: DRAM Refresh
DRAM cells
Row Buffer
DRAM cells lose contents after a while,
Refresh command refreshes all rows at different granularity
How to implement a refresh? What is the latency? How frequent?
DRAM cells are refreshed every 64 ms at normal temperature (< 85◦C).

## Slide 11: DRAM Controller (On-chip)
LLC
Addr. Mapper
RQ WQ
DRAM
Controller
CQ
CQ
CQ
CQ
Command Scheduler
Data bus (burst length= eight beats each of 64-bits)
Command and Address bus
Frequency 800MHz
1066MHz
1333MHz
Frequency 1600MHz
2133MHz
2666MHz
Double Data Rate (DDR)

## Slide 12: DRAM Bandwidth
Names | Memory clock | I/O bus clock | Transfer rate | Theoretical bandwidth
DDR-200, PC-1600 | 100 MHz | 100 MHz | 200 MT/s | 1.6 GB/s
DDR-400, PC-3200 | 200 MHz | 200 MHz | 400 MT/s | 3.2 GB/s
DDR2-800, PC2-6400 | 200 MHz | 400 MHz | 800 MT/s | 6.4 GB/s
DDR3-1600, PC3-12800 | 200 MHz | 800 MHz | 1600 MT/s | 12.8 GB/s
DDR4-2400, PC4-19200 | 300 MHz | 1200 MHz | 2400 MT/s | 19.2 GB/s
DDR4-3200, PC4-25600 | 400 MHz | 1600 MHz | 3200 MT/s | 25.6 GB/s
DDR5-4800, PC5-38400 | 300 MHz | 2400 MHz | 4800 MT/s | 38.4 GB/s
DDR5-6400, PC5-51200 | 400 MHz | 3200 MHz | 6400 MT/s | 51.2 GB/s

## Slide 13: How to attack ?

## Slide 14: Aha !!

## Slide 15: Shared Row [USENIX sec. ‘16]

## Slide 16: Shared Row [USENIX sec. ‘16]

## Slide 17: Side Channel
Side-channel attacks
Row-hits: Fast access
Conflicts: Slow access

## Slide 18: Row-Buffer

## Slide 19: Side-Channel Attack [USENIX sec. ‘16]

## Slide 20: Side-Channel Attack [USENIX sec. ‘16]

## Slide 21: Side-Channel Attack (Remember no actual sharing needed)

## Slide 22: Side-Channel Attack [USENIX sec. ‘16]

## Slide 23: Side-Channel Attack [USENIX sec. ‘16]

## Slide 24: Side-Channel Attack [USENIX sec. ‘16]

## Slide 25: Covert Channel
Covert-channel attacks

## Slide 26: Covert-Channel Attack [USENIX sec. ‘16]

## Slide 27: Covert-Channel Attack [USENIX sec. ‘16]

## Slide 28: Covert-Channel Attack [USENIX sec. ‘16]

## Slide 29: Covert-Channel Attack [USENIX sec. ‘16]