## Slide 1: CS683: Advanced Computer Architecture-2025
Lecture-1: Every Cycle Matters
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: LH-102 is the place to be
CS683 at LH-102 from next week

## Slide 4
Let’s start with programming for Performance
(know your architecture)

## Slide 5
void CS683(int *arr, int size) {
for (int i = 0; i < size-1; ++i)
arr[i] = arr[i+1];
}

## Slide 6: Performance
CPU
CPU time: Time spent running a program
CPU
Execution time: CPU time + IO waiting
CPU time: User time + System (OS) time

## Slide 7: Spell it out (Programming language matters too)
Instructions
Cycles
Program
Instruction
Time
Cycle
(code size)
=
X
X
(CPI)
(cycle time)

## Slide 8: Micro mantra-I: ISA vs Microarchitecture
Same program compiled for different ISAs with or without the same/similar microarchitecture may lead to different runtimes.

## Slide 9: We are almost ready: The game of latency and bandwidth

## Slide 10: Let’s Jump into Memory Hierarchy

## Slide 11: From where do these latency numbers come from?
L3
L1
L2
2 Cycles
12 Cycles
30 Cycles
200 Cycles
DRAM Contr.
Core
CPU
Memory stores CODE and DATA
Processor accesses through LOADs (reads) and STOREs(writes)
Memory Wall

## Slide 12: Hang on!! I got the Mantra!!
Reduction in DRAM accesses ~
Reduction in CPI (cycles per instruction)
WRONG!
First Law of Performance:
  Make the common case fast
Second Law of Performance:
  Make the fast case common
  Amdahl’s law
What if your program is not memory intensive

## Slide 13: Do not ignore the uncommon too
Give me an example

## Slide 14: Let’s Pause and understand: The game of “common” and “uncommon”

## Slide 15: Do not
Over-engineer
Over-think
Over …………………..

## Slide 16: 10,000 Feet View on Caches
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
$$: Cache
Speculation technique
Speculation works because of locality

## Slide 17: Caches
Hardware hash tables 

## Slide 18: Locality (why does it exist?)
Temporal locality:
  Recently referenced items are likely to be referenced again
Spatial locality:
  Items with nearby addresses tend to be referenced again

## Slide 19: Locality: Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial/Temporal
Locality?
temporal
spatial

## Slide 20: Wake-up Test: Improve Spatial Locality
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}

## Slide 21: Cache and DRAM
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
DRAM
4
4
4
10
10
10
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Request: 14
14
Block b is in cache: Hit!
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Request: 12
Block b is not
in cache:Miss!
Block b is fetched from
Memory (replacement)
Request: 12
12
12
12