## Slide 1: CS683: Advanced Computer Architecture-2025
L10: Kya Karein Kya Na Karein (virtual/physical)…
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Small and subtle cache: MMU (PSC, PWC) Cache

## Slide 4: More details
MMU caches are searched parallelly.
Anyways, these are small caches with few entries: 2, 4, 8, 16 entries kinda
PSCL2 will have more entries than PSCL3, and PSCL4
PSCL4 cache usually have two entries only 
For five levels of PTW, we will have PSCL5, 4, 3, 2
Finally, modern processors use multiple PTWs to provide address translation parallelism.

## Slide 5: TLBs and events of interest
Virtual Address
TLB Lookup
Check Permissions
Physical Address
Page Fault Exception
“Protection Fault”
Page Table Walk
Page Fault Exception
“Page Not Present”
TLB Reload
Terminate Process
miss
hit
restart instruction
page present
else
ok
denied
Load Page
machine-dependent
machine-independent
logic

## Slide 6: The Processor Pipeline with the TLBs
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 7: Let’s Dig Deep into TLBs

## Slide 8
int sum = 0;
for (i = 0; i < 2048; i++) { sum += a[i];
}
Calculate miss rate of TLB for data: # TLB misses / # TLB lookups
# TLB lookups?
= number of accesses to a = 2048
# TLB misses?
= number of unique pages accessed
= 2048 / (elements of ‘a’ per 4K page)
= 2K / (4K / sizeof(int)) = 2K / 1K
= 2
Miss rate?
2/2048 = 0.1%
Hit rate? (1 – miss rate) 99.9%
Would hit rate get better or worse with smaller pages?
Answer: Worse
Advanced Computer Architecture
8

## Slide 9: TLB & Workload Access Patterns
Sequential array accesses almost always hit in TLB
  Very fast!
What access pattern will be slow?
  Highly random, with no repeat accesses
Workload A
int sum = 0;
for (i=0; i<2000; i++) { sum += a[i];
}
Workload B
int sum = 0; srand(1234);
for (i=0; i<1000; i++) { sum += a[rand() % N];
}
srand(1234);
for (i=0; i<1000; i++) { sum += a[rand() % N];
}

## Slide 10
time
Sequential Accesses
(Good for TLB)
time
Random Accesses
(Bad for TLB)
…
…
Advanced Computer Architecture
10

## Slide 11: TLB Performance
How can system improve TLB performance (hit rate) given fixed number of TLB entries?
Increase page size
  Fewer unique page translations needed to access same amount of memory
What is the drawback of large pages?
  Increased internal fragmentation
  Tradeoffs, tradeoffs
Most processors support multiple different page sizes
  In 32-bit x86, 4KB and 2MB
  In 64-bit x86, 4KB, 2MB and 1GB
  Programmer (user) makes the choice since they know their program
TLB Reach: Number of TLB entries * Page Size

## Slide 12: TLBs and Context Switches
What happens if a process uses cached TLB entries from another process?
Solutions?
Flush TLB on each switch
  Could be costly; lose all recently cached translations
Track which entries are for which process
  Address Space IDentifier (ASID)
  When loading a TLB entry, tag it with the ASID of the current process (in addition to the VPN)
  When reading TLB, check both VPN and ASID

## Slide 13: TLB Performance
Context switches are expensive
Even with ASID, other processes “pollute” TLB
  Discard process A’s TLB entries for process B’s entries
Architectures often have multiple TLBs and multi-level TLBs
  Level-1: 1 TLB for data, 1 TLB for instructions (smaller, say 64 entries; fast)
  Level 2: combined or separate inst or data TLBs (larger, say 512 entries; slower)
  On a Level-1 TLB miss, first check Level-2 TLB before checking the page table
  MMU caches too: Stores mid-level translations

## Slide 14: A bit Deeper
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Instruction data
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Translate on miss

## Slide 15: Memory Hierarchy with the TLBs
Interconnect
L3
Core 3 L1 $ L2 $
Core 2 L1 $ L2 $
Core 1 L1 $ L2 $
Core 0 L1 $ L2 $
L2 TLB
Page table walker (PTW)
L1 TLB

## Slide 16: Caches: Virtual or Physical
CPU
TLB
cache
lower
hier.
physical cache
CPU
cache
tlb
lower
hier.
virtual (L1) cache
VA
PA
CPU
cache
tlb
lower
hier.
virtual-physical cache
VA
PA
VA
PA

## Slide 17: Synonym Problem
VA1
VA2
Page Table
Data Pages
PA
VA1
VA2
1st Copy of Data at PA
2nd Copy of Data at PA
Tag
Data
Two virtual pages share one physical page
Virtual cache can have two copies of same physical data. Writes to one copy not visible to reads of other!
General Solution: Prevent aliases coexisting in cache
Software (i.e., OS) solution for direct-mapped cache

## Slide 18: Homonym Problem
VA1
Data Pages
PAs
One virtual page maps to two physical pages
Tag may not uniquely identify cache data
Solution: Add ASID with tag
Or
Physical tags
Or
Flush on context switch

## Slide 19: VIPT Caches
If C≤(page_size  associativity), the cache index bits come only from page offset (same in VA and PA)
If both cache and TLB are on chip: index both arrays concurrently using VA bits, check cache tag (physical) against TLB output at the end
VPN
Page Offset
TLB
PPN
Index
BiB
physical
cache
tag
data
=
cache hit?
TLB hit?

## Slide 20
Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
 cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Cases: L + b = k, L + b < k, L + b > k
VPN
L
b
TLB
Direct-map Cache
2L blocks 2b-byte block
PPN
Page Offset
=
hit?
Physical Tag Data
Tag
VA
PA
Virtual Index
k

## Slide 21: Virtual-Index Physical-Tag Caches: Associative Organization
VPN
a
L = k-b b
TLB
Direct-map 2L blocks
PPN |  | Page Offset
=
hit?
Phy. Tag
Tag
VA
PA
Virtual Index
k
Direct-map 2L blocks
2a
=
2a
Data
After the PPN is known, 2a physical tags are compared
How does this scheme scale to larger caches?

## Slide 22: Concurrent Access to TLB & Large L1 The problem with L1 > Page size
PPN | Page Offset | b
VPN | a | Page Offset | b
TLB
Tag
Can VA1 and VA2 both map to PA ?
VA
PA
Virtual Index
PPNa | Data
PPNa | Data
L1 PA cache Direct-map
=
hit?
VA1
VA2

## Slide 23: What if? Think about PIPT, VIPT, PIVT, and VIVT
If C>(page_size  associativity), the cache index bits include VPN  Synonyms can cause problems
  The same physical address can exist in two locations
Solutions?
VPN
Page Offset
TLB
PPN
Index
BiB
physical
cache
tag
data
=
cache hit?
TLB hit?
a

## Slide 24: Golmaal Hai: Any reasons for small L1 cache?
Better answers now 
BTW Apple phones use 196KB L1 caches. Golmaal hai 