## Slide 1: CS683: Advanced Computer Architecture
Lecture 15: It is the Memory Stupid! 
https://www.cse.iitb.ac.in/~biswa/courses/

## Slide 2: Memory Consistency
The memory consistency model of a shared-memory system determines the order in which memory operations will appear to execute to the programmer.
– Core 1 writes to some memory location…
– Core 2 reads from that location…
– Do we get the result we expect?

## Slide 3: Coherence vs Consistency
Formally:
– Coherence: What values can a read return?
• Concerns reads/writes to a single memory location
– Consistency: When do writes become visible to reads?
• Concerns reads/writes to multiple memory locations

## Slide 4: Why it matters?
What value does r2 hold after both processors
finish running this code?
Initial memory contents
a: 0 // memory location a storing zero
flag: 0 // memory location flag storing zero
Processor 1 Processor 2
Store (a), 10; | L: | Load r1, (flag);
Store (flag), 1; |  | if r1 == 0 goto L; Load r2, (a);

## Slide 5: Why it matters?
What value does r2 hold after both processors
finish running this code?
It depends on the order in which processor 2
observes processor 1’s stores!
10 if Store (flag) > Store (a); 0 or 10 otherwise
Initial memory contents
a: 0 // memory location a storing zero
flag: 0 // memory location flag storing zero
Processor 1 Processor 2
Store (a), 10; | L: | Load r1, (flag);
Store (flag), 1; |  | if r1 == 0 goto L; Load r2, (a);

## Slide 6: The definition, An important one
memory consistency model, or, more simply, a memory model, is a specification of the allowed behavior of multithreaded programs executing with shared memory. For a multithreaded program executing with specific input data, it specifies what values dynamic loads may return. Unlike a single-threaded execution, multiple correct behaviors are usually allowed.

## Slide 7: The definition
“A system is sequentially consistent if the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in the order specified by the program”
Leslie Lamport, Turing award winner
Sequential Consistency =
arbitrary order-preserving interleaving
of memory references of sequential programs

## Slide 8: Let’s continue
In-order instruction execution
Atomic loads and stores
SC is easy to understand, but architects and compiler writers want to violate it for performance
Processor 1
Store (a), 10;
Store (flag), 1;
Processor 2
L: Load r1, (flag); if r1 == 0 goto L; Load r2, (a);

## Slide 9: Trend so far 
Architectural optimizations that are correct for uniprocessors often violate sequential consistency and result in a new memory model for multiprocessors

## Slide 10: Memory Consistency Models
Sequential Consistency
  All reads and writes in order
Relaxed Consistency (one or more of the following)
  Loads may be reordered after loads
    e.g., PA-RISC, Power, Alpha
  Loads may be reordered after stores
    e.g., PA-RISC, Power, Alpha
  Stores may be reordered after stores
    e.g., PA-RISC, Power, Alpha, PSO
  Stores may be reordered after loads
    e.g., PA-RISC, Power, Alpha, PSO, TSO, x86
  Other more esoteric characteristics
    e.g., Alpha

## Slide 11: X86 uses TSO (Total Store Order)
We will come back in two weeks time. Once we understand how the processor looks at stores.
So far we have seen how caches see stores 

## Slide 12: DRAM Organization
Channel
Rank
Chip
Bank
Row
Column
Rank 0 with 8 chips
Rank 1 with 8 chips
DIMM

## Slide 13: Rank
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 14: Ranks, Banks, Rows, Columns
Rank 0
Rank 1
DIMM
Bank 0
Bank 1
Bank 2
Bank 3
Multiple Chips

## Slide 15: Ranks, Banks, Rows, Columns
Rank 0
64 bits
16
16
16
16
Bank
Row
Column
Chip
Bank 0
Bank 1
Bank 2
Bank 3
X16 device (DRAM width, # output pins)
16-bit interface: 16 bits from each chip in one go

## Slide 16: Row Decoder and Row buffer
Column mux
Row Decoder
Row Buffer
Each bank has a row buffer
Stores the last used row
2KB

## Slide 17: An Example
2Gb * 8 DRAM Chips (one side of the rank)
Total 16 chips + 2 chips for ECC (for both the ranks)
64 bit + 8 bit ECC interface (72 bit wide DIMM)
Transferring a 64B cache line will take 8 transfers of 8B each
8B will come from 8 chips (8 bits from one chip)
1 bit from each DRAM array assuming 8 DRAM arrays per bank

## Slide 18: DRAM to LLC interaction
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 19: DRAM to LLC interaction
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 20: DRAM to LLC interaction
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 21: DRAM to LLC
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8 cycles (DRAM IO): 1 cycle transfers 8 bytes from a column

## Slide 22: DRAM Address Mapping (One Channel)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
2GB DRAM, 8 Banks, 16K rows, 2K Columns per bank
Row Interleaving: Consecutive rows in consecutive banks
Cache Interleaving: Consecutive cache blocks in consecutive banks

## Slide 23: Row Access
A “DRAM row” is also called a “DRAM page”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 24: Row Buffer hit/miss/conflict
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 25: DRAM Timing Constraints
tRAS: Row address strobe latency
tRP: Precharge latency
tCAS: Column address strobe latency
tRC: Row cycle time: tRAS+tRP

## Slide 26: Row (Page) Policies
Open Page (do not get confused with an OS page)
After an access: Keep the page in the row-buffer
Consecutive accesses to the same page : Row-buffer Hit
On an access to different page: Close the row and open the new one
Closed page:
After an access: Close the page if there are no accesses to the same row in the request queue.
Consecutive accesses to different page : Low latency
On an access to different page: No need to close the row

## Slide 27: 10K view on the latency
Page Empty: ACT + CAS
Page Hit: CAS
Page Miss: PRE+ACT+CAS

## Slide 28: DRAM Refresh
DRAM cells
Row Buffer
DRAM cells lose contents after a while,
Refresh command refreshes all rows at different granularity
How to implement a refresh? What is the latency? How frequent?
DRAM cells are refreshed every 64 ms at normal temperature (< 85◦C).

## Slide 29: PAUSE

## Slide 30: DRAM Controller
LLC
Addr. Mapper
RQ WQ
DRAM
Controller
CQ
CQ
CQ
CQ
Command Scheduler
Data bus (burst length= eight beats each of 64-bits)
Command and Address bus
Frequency 800MHz
1066MHz
1333MHz
Frequency 1600MHz
2133MHz
2666MHz
Double Data Rate (DDR)
Advanced Computer Architecture

## Slide 31: DRAM Bandwidth
Names | Memory clock | I/O bus clock | Transfer rate | Theoretical bandwidth
DDR-200, PC-1600 | 100 MHz | 100 MHz | 200 MT/s | 1.6 GB/s
DDR-400, PC-3200 | 200 MHz | 200 MHz | 400 MT/s | 3.2 GB/s
DDR2-800, PC2-6400 | 200 MHz | 400 MHz | 800 MT/s | 6.4 GB/s
DDR3-1600, PC3-12800 | 200 MHz | 800 MHz | 1600 MT/s | 12.8 GB/s
DDR4-2400, PC4-19200 | 300 MHz | 1200 MHz | 2400 MT/s | 19.2 GB/s
DDR4-3200, PC4-25600 | 400 MHz | 1600 MHz | 3200 MT/s | 25.6 GB/s
DDR5-4800, PC5-38400 | 300 MHz | 2400 MHz | 4800 MT/s | 38.4 GB/s
DDR5-6400, PC5-51200 | 400 MHz | 3200 MHz | 6400 MT/s | 51.2 GB/s
Advanced Computer Architecture