## Slide 1: CS683: Advanced Computer Architecture
Lecture 16: Monsoon over 
Welcome to the land of processors!
https://www.cse.iitb.ac.in/~biswa/courses/

## Slide 2: Vanilla 5-stage pipeline
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
The right place to put the MUX that selects PC+4 and the target is the fetch stage.
The slide shows a vanilla 5-stage pipeline if we just take a single cycle datapath and divide it into five stages.

## Slide 3: Data dependences (hazards)
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
read-after-write
(RAW)
write-after-read
(WAR)
write-after-write
(WAW)
True dependence
anti dependence
output dependence

## Slide 4: Data Hazards
Read-After-Write (RAW)
Read must wait until earlier write finishes
Anti-Dependence (WAR)
Write must wait until earlier read finishes
Output Dependence (WAW)
Earlier write can’t overwrite later write
(WAW hazard: not possible with vanilla 5-stage pipeline)
Advanced Computer Architecture

## Slide 5: Data Hazards (Examples)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)

## Slide 6: Control Hazards: An Example
What do you do with the 3 instructions in between?
How do you do it?
10: beq r1,r3,36
14: and r2,r3,r5 
18: or r6,r1,r7 
22: add r8,r1,r9 
50: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 7: What and Where? Control Hazard
What do we need to calculate next PC?
For Jumps
Opcode, offset, and PC
For Jump Register
Opcode and register value
For Conditional Branches
Opcode, offset, PC, and register (for condition)
For all others
Opcode and PC
In what stage do we know these?
PC - Fetch
Opcode, offset - Decode (or Fetch?)
Register value - Decode
Branch condition ((rs)==0) - Execute (or Decode?)

## Slide 8: Branches: Taken/Not Taken and Target
Instruction Taken known? Target known?
J
After Inst. Decode After Inst. Decode
BEQZ/BNEZ
After Inst. Execute After Inst. Execute

## Slide 9: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?
How?
We know whether it is a branch PC or not in the decode stage. Oh no 

## Slide 10: Branch Predictor: A bit deeper
Three tasks
Is the PC a branch/jump? YES/NO
If Yes, can we predict the direction? Taken or not-taken
If taken, can we predict the target address?

## Slide 11: Let’s see
Program
Counter
Address of the
current branch

## Slide 12: Let’s see
Direction predictor
Program
Counter
PC + 4
taken?
Next Fetch
Address
Address of the
current branch

## Slide 13: Let’s see
target address
Direction predictor
Repository of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + 4
taken?
Next Fetch
Address
hit?
Address of the
current branch

## Slide 14: Two Level Branch Predictors
First level: Global branch history register (N bits)
  The direction of last N branches
Second level: Table of saturating counters for each history entry
The direction the branch took the last time the same history was seen
1 1 ….. 1 0
GHR
(global history register)
00 …. 00
00 …. 01
00 …. 10
11 …. 11
0
1
2
3
index
Pattern History Table (PHT)
previous one

## Slide 15: BTB (Target Address Predictor)
0b0110[...]01001000
2 state bits
Branch
History Table
(BHT)
target address
Branch Target Buffer (BTB)
PC + 4 + Loop
30-bit address tag
0b0110[...]0010
Address of branch instruction
BTB is probed in the fetch stage along with the direction predictor.
A hit in the BTB means the PC is a branch PC.
Branch instruction
BNEZ R1 Loop

## Slide 16: Exception handling and Pipelining
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts
When do we stop the pipeline for precise interrupts or exceptions?
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
Nothing can happen
now?

## Slide 17: Contd.
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 18: Contd.
Hold exception flags in pipeline until commit point for instructions that will be killed
Exceptions in earlier pipe stages override later exceptions for a given instruction
If exception at commit: update cause and EPC registers, kill all stages, inject handler PC into fetch stage