## Slide 1: CS683: Advanced Computer Architecture
Lecture 16: Bye Bye Monsoon;Time for front-end mysteries 
https://www.cse.iitb.ac.in/~biswa/courses/

## Slide 2: Instruction Level Parallelism (ILP)
Scalar pipeline (baseline)
  Instruction overlap parallelism = D
  Peak IPC = 1.0
D
Successive
Instructions
Time in cycles
1
2
3
4
5
6
7
8
9
10
11
12
D different instructions overlapped

## Slide 3: Superscalar Processor
Superscalar (pipelined) Execution
  Instruction parallelism = D x N
  Peak IPC = N per cycle
Successive
Instructions
Time in cycles
1
2
3
4
5
6
7
8
9
10
11
12
N
D x N different instructions overlapped

## Slide 4: Most of the Computer Architecture Courses

## Slide 5: Modern Processors: In-order fetch
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
Advanced Computer Architecture

## Slide 6: Modern Processors: Out-of-order Execute
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
2. LOAD
3. LOAD
5. LOAD
4. MUL
1. SUB
Out of order execute
Advanced Computer Architecture

## Slide 7: Modern Processors: In-order Commit
In-order Instruction Fetch
(Multiple fetch in one cycle)
In-order Completion (commit)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
1. LOAD 
3. LOAD 
4. LOAD 
5. MUL
2. SUB 
2. LOAD
3. LOAD
5. LOAD
4. MUL
1. SUB
Out of order execute
Advanced Computer Architecture

## Slide 8: Modern Processors: In-order Commit
In-order Instruction Fetch
(Multiple fetch in one cycle)
In-order Completion (commit)
1. LOAD
3. LOAD
4. LOAD
5. MUL
2. SUB
1. LOAD 
3. LOAD 
4. LOAD 
5. MUL
2. SUB 
2. LOAD
3. LOAD
5. LOAD
4. MUL
1. SUB
Out of order execute
Reorder buffer (ROB)
1
2
3
ROB head
Advanced Computer Architecture

## Slide 9: Modern Processors: Speculative Execution
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. BE
3. LOAD
4. LOAD
5. ADD
2. SUB
1
2
3
BE reaches ROB head and
then processor realized it is a mistake
Branch Predictor: TRUE
Speculative (wrong path)
instructions
4
Recent Intel processors have 750-entry ROBs
Advanced Computer Architecture

## Slide 10: Modern Processors: Speculative Execution
In-order Instruction Fetch
(Multiple fetch in one cycle)
1. BE
3. LOAD
4. LOAD
5. ADD
2. SUB
1
2
3
BE reaches ROB head and
then processor realized it is a mistake
Branch Predictor: TRUE
Speculative (wrong path)
instructions
4
Instructions 2, 3, and 4
Got squashed
Same happens in the case of a page fault, exception etc…
Advanced Computer Architecture

## Slide 11: Three Great tastes that tastes great together
CPI < 1 : Go for Superscalar
Superscalar increases data hazards: Go for out-of-order
Branch instructions are the problem: Speculative execution
Advanced Computer Architecture

## Slide 12: Front-end Bottleneck (Servers, mobile workloads)
Conditional
Direct Jump
Indirect Jump
Return
Direct Call
Indirect Call
Direct Branch Predictor
Always Taken
Branch Target Buffer
Indirect Branch Predictor
Return Address Stack
Direction
Branches
Branch Target
Advanced Computer Architecture

## Slide 13: Branch instructions
int func(int num) {
int temp = 0;
if(num > 0)
{
temp = temp + 1;
goto loc;
}
switch(temp)
{
case 0: break;
case 1: break;
case 2: break;
case 3: break;
case 4: break;
}
temp--;
loc: return temp;
}
int main() {
func(5);
int (*temp)(int) = &func;
temp(5);
}
func(int):
….
cmp DWORD PTR [rbp-20], 0
jle .L2
add DWORD PTR [rbp-4], 1
jmp .L3
.L2:
cmp DWORD PTR [rbp-4], 4
ja .L4
mov eax, DWORD PTR [rbp-4]
mov rax, QWORD PTR .L6[0+rax*8]
jmp rax
….
ret
main: ….
call func(int)
mov QWORD PTR [rbp-8], OFFSET FLAT:func(int)
mov rax, QWORD PTR [rbp-8]
mov edi, 5
call rax
ret
Conditional
Direct Jump
Indirect Jump
Return
Direct Call
Indirect Call
C++ Code
(b) Assembly Code
Advanced Computer Architecture

## Slide 14: BTB/L1I Capacity/latency Problem
Advanced Computer Architecture

## Slide 15: An Example
High MPKI in front-end structures due to increase in codebase.
Advanced Computer Architecture

## Slide 16: Ideal front-end: Google Web search
Ideal front-end does not provide significant performance improvement on top of ideal BTB (it has ideal ITLB too).
Ideal BTB :- All misses converted to hits.
Ideal L1I :- Misses converted to hits.
Advanced Computer Architecture

## Slide 17: Decoupled Frontend: Welcome to the Mystery
Branch Predictor
i
i
L1I
Fetch Target Queue
Prefetch Request
Instruction Fetch
Instruction Decode
Decoupling allows to run way ahead of demand fetch which helps to reduce the impact of long latency L1I misses
Next Instruction Pointer
Fetch Directed Instruction Prefetching (FDIP)
Thanks to Vedant for this slide

## Slide 18: Decoupled Front-end
Instruction
Direct Jump
Direct Call
Conditional
Indirect Jump
Indirect Call
Return
1
Fetch Target Queue
Insert Branch Target in to BTB
Branch Target
Decode
ITLB
L1I Cache
Direct Branch Predictor
Return Address Stack
Branch Target Buffer
Indirect Branch Predictor
Execute
2
3
4
5
5
5
5
Branch predictor looks ahead even if L1I misses
Advanced Computer Architecture

## Slide 19: FDIP paper (Fetch Directed Instruction Prefetching)
https://cseweb.ucsd.edu/~calder/papers/MICRO-99-FDP.pdf
PIQ: Prefetch Instruction Queue
FTQ: Fetch Target Queue
One entry in FTQ stores 8 instructions

## Slide 20: Benefits
Branch predictor can move ahead and L1I misses can be amortized 
Instruction prefetching?
Hides latency of multi-level branch predictor and BTB
Demands a larger BTB though 
BTB prefetching?
Tradeoffs: BTB capacity vs L1I capacity and latency
What else?
Advanced Computer Architecture

## Slide 21
L2
LLC
DRAM
FETCH Queue
DECODE Queue
Issue Queue
Decode stage stalls, waiting for the instructions to arrive from the outer levels of memory
L1I misses can cause Decode Starvation
I1
I2
I3
L1 I
Empty
 | IF
 | EX
 | ID
I4
I5

## Slide 22: Decode Latency will be there, anyways 
x86 uses variable-length instructions
Size of the decoder cannot be fixed like ARM ISA.
Also, x86 is RISCY ISA  CISC for programmers, RISC for the execution units
One CISC instruction -> many RISC micro-operations
Here is the deal: There is a macro-op queue containing CISC instructions that a pre-decoder logic converts into micro-ops. It can take up to six cycles in the worst case.
Then there will a decode. In general, decoding takes a considerable amount of power and latency.
What can be done? Well, use a cache, called micro-op cache. A hit in the micro-op cache can bypass decode latency.
BTW, which stage in the pipeline, the micro-op cache will be accessed?

## Slide 23: Think about latency and bandwidth again
Front-end latency and bandwidth
Bad speculation (branch predictor, micro-op cache too )

## Slide 24: Students@CS683 after Front-end mysteries