## Slide 1: CS683: Advanced Computer Architecture
Lecture 17: Humid October 
Front-end Mysteries, hmmm, re/de-mystified
https://www.cse.iitb.ac.in/~biswa/courses/

## Slide 2: Decoupled Front-end
Instruction
Direct Jump
Direct Call
Conditional
Indirect Jump
Indirect Call
Return
1
Fetch Target Queue
Insert Branch Target in to BTB
Branch Target
Decode
ITLB
L1I Cache
Direct Branch Predictor
Return Address Stack
Branch Target Buffer
Indirect Branch Predictor
Execute
2
3
4
5
5
5
5
Branch predictor looks ahead even if L1I misses
Advanced Computer Architecture

## Slide 3: FDIP(Fetch Directed Instruction Prefetching)
PIQ: Prefetch Instruction Queue
FTQ: Fetch Target Queue
@Image adapted from FDIP, MICRO'1999

## Slide 4: FTQ directed code prefetching (FDIP)
Advanced Computer Architecture
FTQ is of 24 to 32 entries, one entry in FTQ stores 8 instructions

## Slide 5: Benefits
Branch predictor can move ahead and L1I misses can be amortized 
Instruction prefetching?
Hides latency of multi-level branch predictor and BTB
Demands a larger BTB though 
BTB prefetching?
Tradeoffs: BTB capacity vs L1I capacity and latency
What else?
Advanced Computer Architecture

## Slide 6
L2
LLC
DRAM
FETCH Queue
DECODE Queue
Issue Queue
Decode stage stalls, waiting for the instructions to arrive from the outer levels of memory
L1I misses can cause Decode Starvation
I1
I2
I3
L1 I
Empty
 | IF
 | EX
 | ID
I4
I5

## Slide 7: Decode Latency will be there, anyways 
x86 uses variable-length instructions
Size of the decoder cannot be fixed like ARM ISA.
Also, x86 is RISCY ISA  CISC for programmers, RISC for the execution units
One CISC instruction -> many RISC micro-operations
Here is the deal: There is a macro-op queue containing CISC instructions that a pre-decoder logic converts into micro-ops. It can take up to six cycles in the worst case.
Then there will a decode. In general, decoding takes a considerable amount of power and latency.
What can be done? Well, use a cache, called micro-op cache. A hit in the micro-op cache can bypass decode latency.
BTW, which stage in the pipeline, the micro-op cache will be accessed?

## Slide 8: Think about latency and bandwidth again
Front-end latency and bandwidth
Bad speculation (branch predictor, micro-op cache too )

## Slide 9: Students@CS683 after Front-end mysteries

## Slide 10: We are together: The Bigger Picture (latency and bandwidth)
IF
IF
IFETCH Buffer
DECODE Buffer
Issue
Queue
ID
ROB
Commit
L1 I
L2
LLC
DRAM
L1 D
L2
LLC
DRAM
Front End
Back
End
EX
MA
WB
Micro-op cache

## Slide 11: Some fun questions?
How many Indian students know front-end mysteries bit by bit, cycle by cycle?
1
10
100
1000
10000
100000

## Slide 12: Here are the front-end Ninjas

## Slide 13: O3 (out-of-order) processor
Pipelining: Tries to achieve CPI =1
Hardware scheduling so far: In order execution Instructions after stall must wait even if independent.
Dynamic scheduling: Out of order execution
Hardware lookahead of blocked instructions
Inorder, O3
Inorder fetch, O3 execute, Inorder completion

## Slide 14: Issue Stage??
To enable O3 execution,
We split Decode stage into
Dispatch: Decode instructions, check for structural hazards
Issue: Read operands after all the data hazards are taken care of and issue the instructions to next stage

## Slide 15: Issue Q (instructions enter in-order, leave out-of-order)
Issued
Dispatched

## Slide 16: Why Issue Q or Operation Q?
In-order pipeline: younger ones cannot pass/cross the older instructions
Issue Q: Structure that can hold multiple instructions in-flight, actually not a Q
Register renaming also happens at this stage. More later 

## Slide 17: The Complete Picture First: IBM 360
FP adders
Add1 Add2 Add3
FP multipliers
Mult1 Mult2
FP Registers
Reservation
Stations
To Mem
From Mem FP Op
Queue Load Buffers
Store Buffers
Load1 Load2 Load3 Load4 Load5 Load6
Register renaming through reservation stations

## Slide 18: What is the deal?
Control & buffers distributed with Function Units (FU);
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
Load and Stores treated as FUs with RSs as wells

## Slide 19: Reservation Station
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
Qj,Qk=0 => ready
Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one
exists. Blank when no pending instructions that will write that register.

## Slide 20: Pipeline Stages++
Dispatch and Issue—get instruction from Op Queue
If reservation station free (no structural hazard),
control issues instr & sends operands (renames registers).
To make it simple for the rest of the lecture, let’s assume only issue
Execution—operate on operands (EX) When both operands ready then execute;if not ready, watch Common Data Bus for result
Write result—finish execution (WB)
Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast

## Slide 21: Example: Ready Steady Go!
Instruction status:
Instruction LD
LD MULTD SUBD DIVD ADDD
j k
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
Issue
Exec Write Comp Result
Busy Address
Load1 Load2 Load3
No
No No
Reservation Stations:
Time Name Busy Op
S1
Vj
S2 RS RS
Vk Qj Qk
Add1 Add2 Add3 Mult1 Mult2
No
No No No No
Register result status:
Clock
F0 F2 F4 F6 F8
F10 F12 ... F30
0
FU
Load: 2 cycle FP add: 2 cycles
FP multiply: 10 cycles FP divide: 40 cycles

## Slide 22: Cycle-1
Instruction status:
Exec
Write
Instruction | j | k | Issue | Comp Result |  |  |  | Busy | Address | 
LD | F6 34+ | R2 | 1 |  | Load1 |  |  | Yes | 34+R2 | 
LD | F2 45+ | R3 |  |  | Load2 |  |  | No |  | 
MULTD | F0 F2 | F4 |  |  | Load3 |  |  | No |  | 
SUBD | F8 F6 | F2 |  |  |  |  |  |  |  | 
DIVD | F10 F0 | F6 |  |  |  |  |  |  |  | 
ADDD | F6 F8 | F2 |  |  |  |  |  |  |  | 
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3 Mult1 Mult2
No
No No No No
Register result status:
Clock
F10 F12 ... F30
F0 F2 F4 F6 F8
Load1
1
FU
Load: 2 cycle FP add: 2 cycles
FP multiply: 10 cycles FP divide: 40 cycles

## Slide 23: Cycle-2
Instruction status:
Exec
Write
Instruction | j | k | Issue | Comp Result |  |  |  | Busy | Address
LD | F6 34+ | R2 | 1 |  | Load1 |  |  | Yes | 34+R2
LD | F2 45+ | R3 | 2 |  | Load2 |  |  | Yes | 45+R3
MULTD | F0 F2 | F4 |  |  | Load3 |  |  | No | 
SUBD | F8 F6 | F2 |  |  |  |  |  |  | 
DIVD | F10 F0 | F6 |  |  |  |  |  |  | 
ADDD | F6 F8 | F2 |  |  |  |  |  |  | 
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3 Mult1 Mult2
No
No No No No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
2 | FU |  | Load2 |  | Load1 |  |  | 

## Slide 24: Cycle-3
Instruction status:
Instruction | j | k | Issue | Comp Result |  | Busy | Address
LD | F6 34+ | R2 | 1 | 3 | Load1 | Yes | 34+R2
LD | F2 45+ | R3 | 2 |  | Load2 | Yes | 45+R3
MULTD | F0 F2 | F4 | 3 |  | Load3 | No | 
SUBD | F8 F6 | F2 |  |  |  |  | 
DIVD | F10 F0 | F6 |  |  |  |  | 
ADDD | F6 F8 | F2 |  |  |  |  | 
Reservation Stations:
S1
Vj
S2
Vk
RS RS
Qj Qk
R(F4)
Load2
Time Name Busy Op
Add1 No
Add2 No
Add3 No
Mult1 Yes MULTD Mult2 No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
3 | FU | Mult1 | Load2 |  | Load1 |  |  | 

## Slide 25: Cycle-4
Instruction status:
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2 1 3 4
F2 45+ R3 2 4 F0 F2 F4 3
F8 F6 F2 4 F10 F0 F6
F6 F8 F2
Busy
Address
Load1 Load2 Load3
No
Yes 45+R3
No
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
SUBD M(A1)
Load2
Add1 Yes
Add2 No
Add3 No Mult1 Mult2
Yes MULTD R(F4) Load2
No
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
4 | FU | Mult1 | Load2 |  | M(A1) | Add1 |  | 

## Slide 26: Cycle-5
Instruction status:
Busy Address
3
4
4
5
1
2
3
4
5
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
Load1 Load2 Load3
No
No No
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
2 Add1 Add2 Add3
10 Mult1
Mult2
Yes SUBD M(A1) M(A2)
No No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
5 | FU | Mult1 | M(A2) |  | M(A1) | Add1 | Mult2 | 

## Slide 27: Cycle-6
Instruction status:
Busy Address
3
4
4
5
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Load1 Load2 Load3
No
No No
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Yes SUBD M(A1) M(A2)
Yes ADDD M(A2) Add1
No
Yes MULTD M(A2)
1 Add1 Add2 Add3
9 Mult1 Mult2
Yes DIVD
R(F4)
M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
6 | FU | Mult1 | M(A2) |  | Add2 | Add1 | Mult2 | 

## Slide 28: Cycle-7
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Yes SUBD M(A1) M(A2)
Yes ADDD M(A2) Add1
No
Yes MULTD M(A2)
0 Add1 Add2 Add3
8 Mult1 Mult2
Yes DIVD
R(F4)
M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
7 | FU | Mult1 | M(A2) |  | Add2 | Add1 | Mult2 | 

## Slide 29: Cycle-8
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 2 Add2 Add3
7 Mult1 Mult2
No
Yes ADDD (M-M) M(A2)
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
8 | FU | Mult1 | M(A2) |  | Add2 | (M-M) | Mult2 | 

## Slide 30: Cycle-9
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Reservation Stations:
Time Name Busy Op
S1
Vj
S2 RS RS
Vk Qj Qk
Add1 1 Add2 Add3
6 Mult1 Mult2
No
Yes ADDD (M-M) M(A2)
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
9 | FU | Mult1 | M(A2) |  | Add2 | (M-M) | Mult2 | 

## Slide 31: Cycle-10
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
10
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 0 Add2 Add3
5 Mult1 Mult2
No
Yes ADDD (M-M) M(A2)
No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock |  | F0 | F2 | F4 | F6 | F8 | F10 | F12 ... F30
10 | FU | Mult1 | M(A2) |  | Add2 | (M-M) | Mult2 | 

## Slide 32: Cycle-11
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3
4 Mult1 Mult2
No
No No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
11 | FU | Mult1 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 33: Cycle-12
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3
3 Mult1 Mult2
No
No No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
12 | FU | Mult1 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 34: Cycle-13
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3
2 Mult1 Mult2
No
No No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
13 | FU | Mult1 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 35: Cycle-14
Instruction status:
Busy Address
3
4
4
5
Load1 Load2 Load3
No
No No
7
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3
1 Mult1 Mult2
No
No No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
14 | FU | Mult1 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 36: Cycle-15
Instruction status:
Busy Address
3
4
15
7
4
5
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Load1 Load2 Load3
No
No No
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3
0 Mult1 Mult2
No
No No
Yes MULTD M(A2) R(F4)
Yes DIVD M(A1) Mult1
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
15 | FU | Mult1 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 37: Cycle-16
Instruction status:
Busy Address
3
4
15
7
4
5
16
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Load1 Load2 Load3
No
No No
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3 Mult1
40 Mult2
No
No No No
Yes DIVD M*F4 M(A1)
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
16 | FU | M*F4 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 38: Cycle-55
Instruction status:
Busy Address
3
4
15
7
4
5
16
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
Load1 Load2 Load3
No
No No
10
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3 Mult1
1 Mult2
No
No No No
Yes DIVD M*F4 M(A1)
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
55 | FU | M*F4 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 39: Cycle-56
Instruction status:
Busy Address
4
5
16
8
Instruction LD
LD MULTD SUBD DIVD ADDD
Exec Write
j k Issue Comp Result
F6 34+ R2
F2 45+ R3
F0 F2 F4
F8 F6 F2
F10 F0 F6
F6 F8 F2
1
2
3
4
5
6
3
4
15
7
56
10
Load1 Load2 Load3
No
No No
11
Reservation Stations:
Time Name Busy Op
S1
Vj
S2
Vk
RS RS
Qj Qk
Add1 Add2 Add3 Mult1
0 Mult2
No
No No No
Yes DIVD M*F4 M(A1)
Register result status:
Clock | F0 |  | F2 | F4 | F6 | F8 | F10 | F12 ... F30
56 | FU | M*F4 | M(A2) | (M-M+M(M-M) |  |  | Mult2 | 

## Slide 40: Explicit Register Renaming
Make use of a physical register file that is larger than number of registers specified by ISA
Keep a translation table:
  ISA register => physical register mapping
  Physical register becomes free when not being used by any instructions in progress.
Fetch
Decode/ Rename
Execute
Rename
Table

## Slide 41: Explicit Register Renaming
Rapid access to a table of translations
A physical register file that has more registers than specified by the ISA
Many modern architectures use explicit register renaming + Tomasulo-like reservation stations to control execution.

## Slide 42: Summary
WAR and WAW hazards are primarily eliminated by explicit register renaming. It cannot mitigate RAW hazards. However, it will still rename it so that the processor moves further. Once it runs out of all the registers, it will stall.
Implicit register renaming through reservation stations also mitigates WAR and WAW hazards. For RAW hazards, the processor will wait and stall.