## Slide 1: CS683: Advanced Computer Architecture
Lecture 18: out-of-order, re-order, rename, all demystified 
https://www.cse.iitb.ac.in/~biswa/courses/

## Slide 2: Exceptions and all
Tomasulo (Last week’s out of order with reservation station, out of order completion/commit):
  In-order issue, out-of-order execution, out-of-order completion
Recall: An interrupt or exception is precise if there is a single instruction for which:
  All instructions before that have committed their state
  No following instructions (including the interrupting instruction) have modified any state.
Need way to resynchronize execution with instruction stream (I.e. with issue- order)

## Slide 3: Re-order Buffer (ROB)
Out-of-order commit: What about precise exceptions ?
It would be great to have in-order commit with O3 execute.
The process of an instruction leaving the ROB will now be called as commit.
To preserve precise exceptions, a result is written into the register file only when the instruction commits.
Until then, the result is saved in a temporary register in the ROB.

## Slide 4: Speculative Tomasulo with ROB
Dispatch and Issue—get instruction from Op Queue
If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (“Issue”), renaming
Execution—operate on operands (EX)
When both operands ready then execute; if not ready, watch CDB for result; when both
in reservation station, execute; checks RAW (sometimes called “issue”)
Write result—finish execution (WB)
Write on Common Data Bus to all awaiting FUs
& reorder buffer; mark reservation station available.
Commit—update register with reorder result
When instr. at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer. Mispredicted branch flushes reorder buffer (sometimes called “graduation” or “retire”)

## Slide 5: Issue Q + ROB

## Slide 6: Recovery phase
Instructions fetched and decoded into instruction reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile & memory) is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order Out-of-order In-order
Kill
Kill
Kill
Mis-speculation?
Inject handler PC

## Slide 7: The complete pipeline
Decode & Rename
Reorder Buffer
PC Fetch
Branch Prediction
Update predictors
Commit
Branch
Unit
ALU
MEM
Store
Buffer
D$
Execute
In-Order
Out-of-Order
In-Order
Physical Reg. File
kill
kill
kill
Branch Resolution
kill
Dispatch in-order
and Issue O3

## Slide 8: Transient instruction
A speculative instruction that does not commit is a transient instruction

## Slide 9: Speculative Execution-II
3. In event of mis- speculation, dispose of all new values, restore old values, and re-execute from point before mis- speculation
3. After sure that there was no mis-speculation and there will be no more uses of the old values, discard old values and just use new values
OR
1. Proceed ahead despite unresolved dependencies using a prediction for an architectural or micro-architectural value
2. Maintain both old and new values on updates to architectural (and often micro-architectural) state
After speculation check

## Slide 10: ROB
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
Compar network | Reorder Buffer
 | FP Regs
Reorder Table
Dest Reg
Result
Exceptions?
Valid
Program Counter
Please note that ROB stores the results too  , When commit/retire, it updates registers and memory

## Slide 11
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 12
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 13
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F1,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
If the predicted taken path is wrong,
flush out all instructions from the ROB
and reissue in the correct order
Remember exception/page
fault handling gets resolved
when the instruction
reaches the head of the ROB

## Slide 14: LSQ (Load Store Q): For out-of-order requests into memory hierarchy

## Slide 15: Why LSQ?
ROB makes sure register writes are in order. What about stores or memory writes?
LSQ:
Stores write to LSQ, in an O3. That is why writes are not in critical path 
When store retires, head of LSQ written to L1D
When load executes, access LSQ and L1D in parallel.
Loads are O3. Else there is no point 

## Slide 16: Why LSQ?
For non-memory operations, dependency is checked in the issue stage
But but but, memory addresses are known after execute stage. So when and where to check dependency.
LSQ tracks memory dependences (L-S, S-L, L-L, S-S).

## Slide 17: Continues…. LQ and SQ, On a load request
Select the youngest store older than the load
If hit in the SQ, forward data from SQ
If miss, send it to TLB and L1D.

## Slide 18: The tricky situation
sd x1, (x2)
ld x3, (x4)
When can we execute the load?

## Slide 19: Approaches
In-order:  Then what is the point of out-of-order  
Can execute load before store, if addresses known and x4 != x2
Each load address compared with addresses of all previous uncommitted stores, do not LOAD if STORE address is not known

## Slide 20: Dependency violation continues
LOAD executed before STORE  Fix it 
How?
Select the oldest load that is younger than the store
Use store position, Processor flushes and restarts.

## Slide 21: Address Speculation
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2
Execute load before store address known
Need to hold all completed but uncommitted load/store addresses in program order
If subsequently find x4==x2, squash load and all following instructions => Large penalty for inaccurate address speculation

## Slide 22: Better Approach? Predict, Load-store dependency predictor
Predict, which loads or load store pairs will cause violations.
Loads must execute in-order with respect to older stores.
Load execution requires knowledge of all older store addresses. If some older store address is not available yet, wait 
There is a store buffer (along with store Q) that deals with the committed store instructions and pushing data into cache hierarchy.

## Slide 23: More subtle
Store queue deals with in-flight instructions.
Once a store instruction retires from the pipeline and is no longer speculative, its data and address are transferred from the store queue to the store buffer.

## Slide 24: Do not Forget the Bigger Picture
Issue Q
ROB
RS
LQ
SQ
Store buffer

## Slide 25: Is this relevant in 2023? Intel Skylake for you
Intel latest processor

## Slide 26: Apple hai Kya?
Apple latest processor

## Slide 27: What about AMD?
AMD latest processor

## Slide 28: Devil is in the details

## Slide 29: Connect All now
Memory systems, caches, TLBs, MSHRs, LSQs, O3 execution, ROB, …..
Can you guess: An L3 cache miss may not cause performance degradation, why? When? 
What next: Energy/Power of a modern processor

## Slide 30: SMT processors: ILP to TLP (Thread-level)

## Slide 31: Single-thread to SMT (Yes IBM, no Apple)
What is a thread in hardware? It is a PC, Thread level parallelism
Superscalar
Fine-Grained Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5 Idle slot
Time (processor cycle)
Advanced Computer Architecture

## Slide 32: IBM Power Series
Power 4
Power 5
2 fetch (PC),
2 initial decodes
2 commits (architected register sets)
Advanced Computer Architecture