## Slide 1: CS683: Advanced Computer Architecture
The last lecture: 10K feet view on architecture security

## Slide 2: Information leakage
CIA: Confidentiality, Integrity, Availability

## Slide 3: Information leakage
Availability: did the computational resource carry out the task at all?
CIA: Confidentiality, Integrity, Availability
Confidentiality: was data being computed upon not revealed to an un-permitted party?
Integrity: was the computation performed
correctly, returning the correct result?

## Slide 4: Channels of Interest
Physical channels
Power, EM,
sound, etc.
Timing channels
Response time
Microarchitectural channels
Microarch events (e.g., timing, perf. counters, mem interleavings)
Processor
Victim
Processor
Victim
Processor
Victim
Attacker
Attacker requires measurement equipment  physical access
Attacker may be remote (e.g., over an internet connection)
Attacker may be remote, or be co-located

## Slide 5: Side/Covert Channel
A side channel is an unintended communication between two or more parties
A covert channel is an intended communication between two or more parties
(you upload a video on YouTube to communicate some information to your friends, if Gmail, whatsapp, call is not allowed)
In both cases:
Communication should not be possible, following computing systems semantics
The physical channel used for the communication can be the same
Side channels  unintended  need de-noising Covert channels can show “best case” leakage

## Slide 6: Scope of these channels
Inter-process(application) communication that can violate privilege boundaries
Infer information from application’s data-dependent HW resource usage
Side/covert channels not in any interface specification (e.g. ISA).
Therefore stealthy
Sophisticated mechanisms needed to detect channel
No permanent indication one has been exploited

## Slide 7: Let’s try to send a bit
Two processes can agree on “dead drops”
Cache:
# ways
# sets

## Slide 8: Let’s try to send a bit
Process 1 (Sender)
Two processes can agree on “dead drops”
Cache:
# ways
Process 2 (Receiver)
# sets

## Slide 9: Let’s try to send a bit
Process 1 (Sender)
Process 2 (Receiver)
t1 = rdtsc() repeat N: fill set i t2 = rdtsc()
If (t2 – t1 > THRESH) read ‘1’ Else read ‘0’
Two processes can agree on “dead drops”
Cache:
# ways
# sets
if (send ‘1’) repeat N: fill set i else
idle

## Slide 10: How is it different from legitimate communication
include <socket.h>
void send(bit msg) {
socket.send(msg);
}
bit recv() {
return socket.recv(msg);
}
void send(bit msg) {
// pressure on cache
}
bit recv() { st = time();
// pressure on cache
return time() – st > THRESH;
}
Normal communication
Covert Channel communication
send(msg)
recv()
Channel

## Slide 11: From Covert to Side Channel
Hardware resource
Victim
Attacker
if (send ‘1’) Use resource else
idle
Covert channel:
if (secret)
Use resource
else
idle
Side channel:
t1 = rdtsc() Use resource t2 = rdtsc()
if (t2 – t1 > THRESH) read ‘1’ else read ‘0’

## Slide 12: From Covert to Side Channel
Hardware resource
Victim
Attacker
if (send ‘1’) Use resource else
idle
Covert channel:
if (secret)
Use resource
else
idle
Side channel:
t1 = rdtsc() Use resource t2 = rdtsc()
if (t2 – t1 > THRESH) read ‘1’ else read ‘0’

## Slide 13: Side/Covert Channel: Summary
Side-channel attacks
Spy
Victim
Covert-channel attacks
Let’s play
Oh Yes!!

## Slide 14: Information leakage in the real world
Modular exponentiation, be mod n
Exponent e is used for decryption
Attacker tries to get the e
multiply
square
reduce

## Slide 15: Information leakage
Modular exponentiation, be mod n
Exponent e is used for decryption
Attacker tries to get the e
ei = 0, Square Reduce (SR)
ei = 1, SRMR
multiply
square
reduce

## Slide 16: Clflush instruction
Invalidates from every level of the cache hierarchy in the cache coherence domain the cache line that contains the linear address specified with the memory operand. If that cache line contains modified data at any level of the cache hierarchy, that data is written back to memory. The source operand is a byte memory location.

## Slide 17: Flush attack
17
Step 0:Spy maps the shared library, shared in the cache
Step 1:Spy flushes the cache block
LLC
Step 2: Victim reloads the cache block
Step 3: Spy reloads the cache block (hit/miss)
Hit, Voila

## Slide 18: Spectre and Meltdown

## Slide 19: Spectre in Action: Fasten Your Seat Belts
int CS773Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS773Array))
x = CS773Array[attacker]
y=MyArray[CS773Array[attacker]*512]
DRAM LOAD (make sure you
thrash all from cache)
DRAM LOAD (make sure you thrash all from
cache)
X is the secret that is not accessible to the attacker

## Slide 20: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
int CS773Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS773Array))
y = MyArray[CS773Array[attacker]*512]

## Slide 21: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
Attacker has mis-trained it  
T T T T T T T T T T T
How? By using values less than 3 always  
int CS773Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS773Array))
y = MyArray[CS773Array[attacker]*512]

## Slide 22: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
Attacker has mis-trained it  
Processor is on the wrong-path   
int CS773Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS773Array))
y = MyArray[CS773Array[attacker]*512]

## Slide 23: Branch Predictor and Speculative Execution
Branch predictor returns TRUE 
Attacker has mis-trained it  
Processor is on the wrong-path   
Branch resolution latency 200 cycles    
int CS773Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS773Array))
y = MyArray[CS773Array[attacker]*512]

## Slide 24: Within these 200 cycles 
CS773Array[4] is in L1/L2/L3 
The address is in the cache  
Yes, you guessed it right: F+R, P+P cache attacks   
int CS773Array = [100, 200, 300];
int attacker = 4;
if (attacker < sizeof(CS773Array))
y = MyArray[CS773Array[attacker]*512]

## Slide 25: After say 200 cycles
y = MyArray[CS773Array[attacker]*512]
LOAD MyArray[0] 60 ns
LOAD MyArray[512] 60 ns
LOAD MyArray[1024] 5 ns Bingo !! CS773Array[attacker] = 2
Processor realized it was a mistake and
squashed all wrong path instructions
But cache has the data 

## Slide 26: What if myarray is not shared with the attacker?
Still it is possible to do Spectre attack 
How?
CS773Array[attacker] = 0, you access set 0
CS773Array[attacker] = 1, you access set 1
CS773Array[attacker] = k, you access set k
So, in summary, the attacker can do prime and probe on sets and check which sets show latency difference

## Slide 27: Summary of Spectre Attack: As an attacker
"Two paths diverged in a branch, and I— I took the one less traveled by, And that has made all the difference.“ 
-Frobert Rost, The Path/Road Not Taken
"Two paths diverged in a branch, and I— I took the one more traveled by, And that has made all the difference.“ 
-Frobert Rost, The Path Taken

## Slide 28: Meltdown: The O3 Curse!!
raise_exception();
// line below is never reached
secret=KernelArray[data*4096];
secret=KernelArray[data*4096];
2. raise_exception();
Out-of-order (O3) as
it has no dependency
Kernel Trap
What about page-fault?
https://meltdownattack.com/meltdown.pdf

## Slide 29: Rowhammer
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Repeatedly opening and closing a row induces disturbance errors in adjacent rows
Opened
Closed

## Slide 30: Rowhammer (Reliability issue)
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Opened
Closed
“It’s like breaking into an apartment by repeatedly slamming a neighbor’s door until the vibrations open the door you were after” – Motherboard Vice

## Slide 31: The Code Please
DDR3
DRAM Module
x86 CPU
X
111111111
111111111
111111111
111111111
111111111
111111111
Avoid cache hits
  Flush X from cache
Avoid row hits to X
  Read Y in another row
Y

## Slide 32: The code please
Y
X
111111111
111111111
111111111
111111111
111111111
111111111
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
1111
1111
011011110
110001011
101111101
001110111

## Slide 33: Why? Electromagnetic Coupling
  Toggling the wordline voltage briefly increases the voltage of adjacent wordlines
  Slightly opens adjacent rows  Charge leakage

## Slide 34: Nah Actually a Security issue
PTHammer (hammering into the page table)
Kernel Privilege Escalation
Think about ML/DL models