## Slide 1: CS683: Advanced Computer Architecture-2025
L6: Time to Shift the Gears
(Cache Management Techniques)
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Types of applications and cache behaviors

## Slide 4: Reducing Miss rate (MPKI)

## Slide 5: Cache Content Management
Cache Promotion Policy: On a future hit (block i), promote to MRU
LRU causes thrashing when working set > cache size
a
b
c
d
e
f
g
h
Cache Eviction Policy: On a miss (block i), which block to evict (replace) ?
MRU LRU
SET A
i
a
b
c
d
e
f
g
Cache Insertion Policy: New block i inserted into MRU.
MRU LRU
SET A

## Slide 6: Common Cache Access Patterns
Recency friendly (a1, a2,….ak, ak-1, ….a2, a1)N
Thrashing (a1, a2,….ak)N
[k > cache size]
Streaming (a1, a2,….a∞)N
Combination of above three

## Slide 7: LRU limitations
LRU exploits temporal locality
Streaming data (a1, a2, a3,….a∞): No temporal locality,
No temporal reuse
Thrashing data (a1, a2, a3,….an) [n>c] Temporal locality exists. However, LRU fails to capture.

## Slide 8: BTW, LRU is not implemented @commercial machines

## Slide 9: Why?
Implementation complexity
Power overhead

## Slide 10: Bimodal Policy [ISCA ‘07]
if ( rand() <  ) 
Insert at MRU position; else
Insert at LRU position;
For small : BIP retains thrashing protection of LRU insertion policy.
Infrequently insert lines in MRU position

## Slide 11: Dynamic Insertion Policy (DIP): Celebrated technique in the community
SDM (LRU-sets)
Follower Sets
SDM (BIP-sets)
n-bit PSEL
+
miss
–
miss
MSB = 0?
YES
Use LRU
No Use BIP
SDM – Set Dueling monitors PSEL – n-bit saturating counters for deciding a policy

## Slide 12: RRIP [ISCA ‘10]
RRP Tail
3
2
1
‘intermediate’ ‘far’ ‘distant’
0
‘near-
Re-reference Prediction Value RRPV (n=2):
Qualitative Prediction:
RRP Head
h g f e d c b a
immediate’
Intuition: New cache block will not be re-referenced soon.
Replaces block with distant RRPV.
Insert with RRPV=2, Evict with RRPV=3 promote blocks with RRPV=0.
Static RRIP (Single core) and Thread-Aware Dynamic RRIP (SRRIP+BRRIP, multi-core, based on SDMs).

## Slide 13: 2-bit state machine
0
Imme- diate
1
Inter- mediate
3
distant
re-reference
No Victim
re-reference
eviction
re-reference
No 2
Victim far
No Victim
(SRRIP)
Scan-Resistant
insertion
( BRRIP )
Thrash-Resistant
insertion

## Slide 14: What about L1 and L2 caches?
What about L1I cache and L1D cache?

## Slide 15: Project Topic 1:
Caches for desktop, client/server, mobile workloads
Application specific cache designs