## Slide 1: CS683: Advanced Computer Architecture-2025
L7: Time to Shift the Gears
(Hardware Prefetching)
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Reducing Miss rate, Nah, Miss Latency
Hardware Prefetching

## Slide 4: Hardware Prefetching
What?
Latency-hiding technique - Fetches data before the core demands.
Why?
Off-chip DRAM latency has grown up to 400 to 800 cycles.
How?
By observing/predicting the demand access (LOAD/STORE) patterns.

## Slide 5: An example
L2
Prefetcher
X+3
Core
❶
❷
❸
❹
❺
X+3
HIT
X+2 X+1 X

## Slide 6: Prefetch Degree
Prefetch Degree: Number of prefetch requests to issue at a given time. Think about MSHR size now. It should go up to accommodate prefetching.
L2
L3/DRAM
Prefetcher
X
Demand Access
X+1 |  |  | 
X+1 | X+2 |  | 
X+1 | X+2 | X+3 | X+4

## Slide 7: Prefetch Distance
Prefetch Distance: How far ahead of the demand access stream are the prefetch requests issued?
 |  | X |  |  | Y | 
demand
access
Prefetch-distance Y = X + 4
Y = X + 8 Y = X + 16
prefetch

## Slide 8: The Simplest one
Next Line: Miss to cache block X , prefetch X+1. Degree=1, Distance=1
Works well for L1 Icache and L1 Dcache.
Next N Line: Miss to cache block X , prefetch X+1, X+2, ….. X+N, Degree=N, Distance= min. 1 and max. N

## Slide 9: What about this?

## Slide 10
for (i = 0; i < N; i=i+16)
sum +=c[i];
c[0]
c[16]
c[32]
c[48]
...
2
2
2
L1
L0
L2
L3
Page
L4
L5
L6
Cache line size of 64B
IPX: PC: LOAD
*Loops over arrays/structures
Stride=difference in cache line accesses

## Slide 11: IP-stride prefetching [Intel, AMD, ARM, IBM]
PC
effective address
instruction tag
previous address
stride
state
-
+
prefetch address

## Slide 12: Stream prefetcher [Intel, IBM, ARM, AMD]
100 | 102 | 104 | 503 | 504 | 501 | 499
Tr
ained
miss sequence
503
504
501
Fail!
Trained!
100 102 104 504 501 499 !
1st 2nd 3rd 1st 2nd 3rd
miss miss miss miss miss miss
Training: Consecutive misses in the same direction.
Prefetching: Next k lines in the stream direction.

## Slide 13: Stream prefetcher (Region based) in action
 |  |  | Monitored region |  |  |  |  |  | 
prefetch degree
original addr
prefetch distance
Stream direction
memory access
start addr end addr

## Slide 14: Quantifying prefetchers
PrefetchAccuracy(i)  Prefetchhits(i)
Prefetchissued(i)
Lateness(i)  Prefetchlate(i)
Prefetchhits (i)
Pollution(i)  LLC Poll(i)
Demandmisses(i)
Prefetched Block in the Cache.
Prefetched Block Still on its way
Prefetched Block evicted a demand block that will be reused
Coverage(i)  Prefetch Hits(i) Prefetch Hits (i)  Demandmisses(i)
Fraction of misses avoided