## Slide 1: CS683: Advanced Computer Architecture-2025
L8: August over, final lecture before the world of Maya
(Connecting all@August)
https://www.cse.iitb.ac.in/~biswa/courses.html

## Slide 2: Phones (smart/non-smart) on silence plz, Thanks

## Slide 3: Quantifying prefetchers
PrefetchAccuracy(i)  Prefetchhits(i)
Prefetchissued(i)
Lateness(i)  Prefetchlate(i)
Prefetchhits (i)
Pollution(i)  LLC Poll(i)
Demandmisses(i)
Prefetched Block in the Cache.
Prefetched Block Still on its way
Prefetched Block evicted a demand block that will be reused
Coverage(i)  Prefetch Hits(i) Prefetch Hits (i)  Demandmisses(i)
Fraction of misses avoided

## Slide 4: Can Prefetching heuristics help cache management too?
Yes
How? Coarse-grained decisions
Think about cache replacement and prefetch interactions too 
Prefetched blocks get filled through the same route of L3, L2, and then L1D
Low accuracy will pollute cache, eat bandwidth too.

## Slide 5: Cache Hierarchy with prefetcher and prefetch Q
L1/L2 Prefetcher
L2/L3
MSHR
Fill Q
WB Q
DRAM Ctrller

## Slide 6: Is this all real?
https://chipsandcheese.com/p/hot-chips-2023-arms-neoverse-v2

## Slide 7: This is it

## Slide 8: State-of-the-art prefetchers [ISCA 20, MICRO 22, MICRO 23, MICRO 24] and IITB

## Slide 9: Project Topic-2
Pushing the limits of hardware prefetchers
Application specific hardware prefetchers

## Slide 10: Single-thread performance

## Slide 11: Some more Micro ideas
Pipelined cache: Tag, indexing, data transfer (3 stage pipeline)
Banked cache: Discussed before, improves bandwidth without compromising latency. Yes indexing will now have bank bits.
Skewed Cache

## Slide 12: Skewed Cache
Address
Hash0
Hash1
Different hash functions for different banks.

## Slide 13: Life and Death in Cache 
Live blocks: referenced again before eviction
Dead blocks: not referenced before eviction
On average, 80% of the cache blocks are dead.

## Slide 14: Dead-block predictors in town
Coarse-grained decisions again
PC-based
Region-based
If a PC always brings deadlines, then can we bypass the cache 
Why not?

## Slide 15: What else? Every Cycle Matters
Off-chip predictors [Extremely new idea in town]
Still in a baby academic research stage
Predict which loads will go to DRAM always, and directly go to DRAM  hides cache access latency 